Linux Chapter 8:
Wireless Networks
Joseph Livesay • Julian Richen

---
Introduction
Wireless networks have become prevalent in almost every aspect of our everyday lives
- However as the amount of wireless communication increases, the amount of security needed to fortify and protect users will also increase
- This chapter focuses on auditing wireless networks in the Linux environment
Introduction

---
Wireless Setup - Linux Wireless Chipsets
Wireless Setup - Linux Wireless Chipsets
Atheros
  - Supports the MADWifi (Multiband Atheros Driver for Wireless Fidelity) for native compatibility with Linux
  - Has the ability to audit both the access point and the wireless clients connected to it

---
Wireless Setup - Linux Wireless Chipsets
Wireless Setup - Linux Wireless Chipsets
Conexant PrismGT
  - Allowed Linux users to gain full access of chipsets from Prism54
  - Uses built in Wireless-Tools (ex. iwconfig, iwpriv, etc..)
    - As opposed to previous chipsets like the Atheros
  - Uses a mix of FullMAC and SoftMAC Cards
    - FullMAC requires firmware to be loaded WNIC
    - SoftMAC offload work done on firmware to host machine

---
Wireless Setup - Linux Wireless Chipsets
Wireless Setup - Linux Wireless Chipsets
Ralink and Serialmonkey
  - Only supports the ability to monitor traffic, cannot be used as an access point for security auditing
- Intel Centrino and IPW2200
  - One of the most common wireless chipsets in computing
  - Only natively supports monitoring mode
    - Limited usage in its native form as it does not support frame-injection
  - There is a master mode driver that is currently in development, however it requires additional installing onto the Linux machine

---
Wireless Setup - Linux Wireless Chipsets
Wireless Setup - Linux Wireless Chipsets
Other Wireless Chipsets
  - Many other chipsets exist for WNIC
    - Ex: from Broadcom and Texas Instruments
  - Linux support may be patchy
  - Avoid them if possible, if you can’t:
- NDISwrapper/Driverloader
  - A wrapper for the Windows WNIC driver
    - Nearly every WNIC ships with a Windows driver built in
  - Acts as an abstraction layer and allows Linux machines to use functionality found in the Windows driver
  - Not full-proof
    - Does not allow monitor or master mode, which allows using full power of chipset

---
Combating attacks from Linux wireless chipsets
Combating attacks from Linux wireless chipsets
The appropriate measures of defense against an attacker utilizing Linux wireless chipsets and tools are:
  - Drying up the supply of Linux-native-supported wireless chipsets
  - Stopping the development of the Linux-native wireless drivers that enable the use of the hardware
  - Running RF- or protocol-based denial-of-service (DoS) attacks against the attacker’s hardware
- The first two options are practically impossible, while launching an RF attack is usually impossible because typically the attacker is only passively listening on wireless traffic
- The only plausible defense is a protocol-based DoS attack, however this can be an illegal activity if attacking the wrong target

---
Wireless Hacking Physics
Wireless Hacking Physics

---
Radio Frequency
Radio Frequency
The transmission medium which 802.11x operates on
  - Other protocols also work on radio frequency [802.15 (Bluetooth) and 802.16 (WiMax)]
- It is important to understand RF signals as we can use them to exploit WNIC
- RF exists as a waveform and can experience noise and other forms of signal loss

---
Radio Frequency
Radio Frequency
Frequency of an RF signal is how often the signal repeats or “cycles” in a given time period (normally 1s)
  - Ex: 2.4 Ghz cycles 2,412,000,000 times a second
- We need the wavelength to determine the range which a signal can travel
  - You can find a wavelength by using:
    - Wavelength = Speed of Light * (1/Frequency)
  - Normally APs limit the “effective” range to a 100-meter bubble
  - Using a Cantenna we can pick-up signals far away from the bubble

---
Impact of Frequency and Wavelength on Offense and Defense
Impact of Frequency and Wavelength on Offense and Defense
- Utilizing the frequency of the access point, the wavelength it is producing can be derived
- Using this information, a cantenna can be made that utilizes this calculated wavelength
  - A cantenna has the ability to far extend the normal operating range of an access point, allowing a hacker to access the network far outside any physical barriers that might exist and to retain their anonymity
- Physically reducing the effective range of the access point is a defense against this form of attack

---
Amplitude
Amplitude
The amplitude of a wave determines the amount of electrical energy it possesses
  - The stronger the amplitude, the stronger the signal from the access point is
- The more amplitude that an attacker can get, the easier it will be to decode signal because they will have more data to utilize
- This can be defended against by lowering the amplitude from the access point to a level appropriate for its range

---
Non-Protocol-Based DoS
Non-Protocol-Based DoS
Noise is undesirable interference of RF
  - Can distort signal properties
- Noise can be man-made or natural
  - Ex. Military sending noise to interfere with enemy signals (ECM)
  - Ex. Natural barriers and signal preventing material
- Signal encoding & decoding can help reduce noise or parse signals with a lot of noise, but not always
  - Ex. Direct Sequence Spread Spectrum (DSSS)
  - Ex. Orthogonal Frequency Division Multiplexing (OFDM)
- In the end noise based DoS attacks will override attempts to parse noise interfered signals

---
Attenuation
Attenuation
Attenuation is the reduction of amplitude
  - Caused by physical obstruction or atmospheric interference on the RF waves
- Attenuation can occur in three different ways:
  - Reflection
  - Refraction
  - Absorption
- The sum of all effects of attenuation form a quantity called path loss
  - Measured in decibels (dB)
- In order to achieve the best amplitude from the signal, an attacker must take into account all aspects of attenuation

---
RF Hacker Improvement Kit: Antennas and Gain
RF Hacker Improvement Kit: Antennas and Gain
- Signals are often not strong enough to “hack” from range
- Use the knowledge of RF to create devices to enhance signal reception and transmission
- Antennas come in multiple forms
  - Omnidirectional
    - Sends signals in multiple directions
    - What most store-bought consumer APs are
  - Direct Antenna
    - Sends signals in one direction, but much stronger than Omnidirectional
    - Mostly seen on TVs

---
RF Hacker Improvement Kit: Antennas and Gain
RF Hacker Improvement Kit: Antennas and Gain
Yagi-Uda antenna design

---
RF Hacker Improvement Kit: Antennas and Gain
RF Hacker Improvement Kit: Antennas and Gain
Yagi-Uda antenna RF footprint

---
RF Hacker Improvement Kit: Antennas and Gain
RF Hacker Improvement Kit: Antennas and Gain
- Using the antenna designs found on the previous slides we can create an antenna that can pick-up and transmit RF signals from a much greater range than a normal AP.
- The Yagi-Uda antenna can transmit a signal 1.5km if both APs are setup correctly and have the power
- Using one of these antennas directed at a normal household AP we can pick-up signals far away
  - All that is left is to break the APs wireless security
- This is the main concept of a Cantenna and “hacking” RF signals

---
Defense against RF exploitation
Defense against RF exploitation
Defending against the exploitation of an access point’s wave transmission centers around limiting the range of its transmission.
  - Primarily using attenuation.
- Placing obstacles such as high-density cubicles, wire-mesh barriers, and aluminum-based paint can distort the RF signal to a point it can’t be utilized unless it is within these obstacles
- Also utilizing RF equipment with shorter wavelengths can increase the effect of attenuation

---
RF SPECTRUM ANALYSIS
RF SPECTRUM ANALYSIS

---
Identifying Frequency Usage and Patterns
Identifying Frequency Usage and Patterns
- The investigating and identifying of patterns in RF activity in a given range of frequencies is the core of RF spectrum analysis
- Use a RF spectrum analyzers to receive, record, and plot RF energy in a given frequency band
- You can use spectrum analyzers for good by analyzing frequency range for other APs operating in the same RF
  - Helps to determine a better range to broadcast in (ie. 5Ghz if a lot of noise already exists on 2.4Ghz)

---
Defending Against RF Spectrum Analysis
Defending Against RF Spectrum Analysis
- Very difficult to defend against since it is a passive attack
- You can attempt to identify an attacker by looking around for anyone with a hand-held device or WiFi dongle
  - A device is required to pick-up the signal
  - However, not all devices are used for attacks
    - Someone might have a WiFi dongle for legitimate reasons

---
EXPLOITING 802.11
EXPLOITING 802.11

---
802.11
802.11
- 802.11 is the most commonly used wireless technology for IP-based data
- Frame analysis is a common exploit of the 802.11 communication technology

---
Frame Analysis
Frame Analysis
- Frame transmission can be a large target for manipulation because they do not have any form of encryption
- In order to avoid collisions with data transmissions, the access point and client send frames of data back and forth to each other to confirm when they’re able to receive and transmit data
- If an attacker is able to bombard the receiving channel of the access point, they can control the flow of frames requesting transmission

---
Frame Analysis
Frame Analysis
- By analyzing the frames being passed in the network, an attacker can determine if the frame is being sent to the access point or from the access point.
- Once a frame has been sent, the attacker can spoof a frame to cause dissociation from the network, starting a DoS attack which can spread throughout the network
- This can also be used to sniff out data in the frame

---
Defending Against 802.11 Frame Analysis
Defending Against 802.11 Frame Analysis
- Like RF Spectrum Analysis, Frame Analysis is difficult to counter as it is a passive attack
- One possible counter is to send out crafted frames that exploit a DoS vulnerability in the attackers WNIC chipset
  - This assumes you know the attackers chipset (not likely)
  - Any other legit user with the same chipset would be affected
- In order to really counter attack the 802.11 spec would need to be re-written to protect frame headers and/or introduce mutation based authentication on packets
  - Up to IEEE, not likely for the time being

---
WIRELESS AUDITING ACTIVITIES AND PROCEDURES
WIRELESS AUDITING ACTIVITIES AND PROCEDURES

---
Keep in mind
Keep in mind
When you or a business have a wireless network auditing is needed to verify integrity and wireless exposure of the network
  - Compatible with OSSTMM-based security test
- Attackers don’t need to keep in mind wireless policies
  - Auditors and white-hat hackers do

---
Auditing Wireless Policies
Auditing Wireless Policies
A security policy is critical for managing a companies security
  - Often the most neglected area of an organizations
- Some companies believe they don't need one if they don't have a wireless network, wrong
- Users that plug rogue AP device can create wireless networks that act as the companies network
  - Can fool users and cause damage

---
Auditing Wireless Policies
Auditing Wireless Policies
Other non-AP devices may be introduced that would require an wireless security policy, ex.
  - wireless-enabled laptops
  - PDAs
  - handphones
- Some users may bring their own devices creating hotspots and cause security holes in a network with no security policy
- Auditing is required to enforce rules

---
Auditing Wireless Policies
Auditing Wireless Policies
Auditing policy should expand into:
  - Access policy
  - Authentication policy
  - Accountability policy
  - Availability
  - System and network maintenance policy
  - Acquisition guidelines
  - Violations reporting
  - Audit policy

---
Assembling a Linux-based Auditing/Hacking Platform
Assembling a Linux-based Auditing/Hacking Platform
Common software and hardware:
  - Wireless Sniffers
  - Wireless Frame Injectors
  - WEP/WPA-PSK Crackers
  - Wireless MITM
  - Wireless Client Auditing
  - Wireless Fuzzers
  - Wireless Fingerprinting
  - Specialized Wireless Auditing LiveCD Toolkit

---
Wireless Sniffers
Wireless Sniffers
Come under two categories
  - Passive Sniffer
    - Does not send any kind of data to WNIC
    - Picks-up wireless frames when WNIC is broadcasting in RFMON mode
  - Probing Sniffer
    - Sends our data to WNIC in probe request
    - Used when trying to find out APs in area
    - Needed when you need to find out information about AP
- Common wireless sniffers on Linux include
  - Kismet, Airodump-ng, and Prismstumbler

---
Wireless Frame Injectors
Wireless Frame Injectors
- Allows an attacker to customize frames to cause dissociation from the network
- Creates frames that can be used in any situation with 802.11
- Can fool users into thinking they are accessing a legitimate access point
- Used in with frame analysis

---
WEP/WPA-PSK Crackers
WEP/WPA-PSK Crackers
- Tools used to crack WEP and WPA-PSK encryption
- WEP Attack
  - Attack happens by capturing enough WEP encrypted data frames so tools can find a pattern
- WPA-PSK Attack
  - Uses Password-Based Key Derivation Function v2.0 (PBKDF2) math formula to break encryption
- Tools include
  - WEPCrack, Airsnort, Aircrack-ptw, and Aircrack-ng
  - Cowpatty, Aircrack-ng v0.7 (For WPA-PSK)

---
Wireless MITM
Wireless MITM
- A tool that establishes a man-in-the-middle attack
- Sets up the wireless chipset to master mode
- Forms a DHCP server, an HTTP server, and a DNS server on the attackers computer so that the clients think they are accessing a legitimate AP
- Directs traffic through to a legitimate network, but the attacker simultaneously sniffs all of their data

---
Wireless Client Auditing
Wireless Client Auditing
Many devices that have WNIC (laptops, phones, etc..) have wireless chipsets that are left on
  - Attackers can use tools to trick client device into connecting to them
  - Assuming the client is connected to the wired network as well the Attacker now uses the established wireless network to the client device to bridge them to the connected wired network
- Tools:
  - Probemapper, Karma, and Hotspotter

---
Wireless Fuzzers
Wireless Fuzzers
- Tools that generate a series of wireless frames and throw them at wireless devices at a configurable speed and quantity
- Used to test wireless drivers found in Linux Kernel
- Tools:
  - Fuzz-e, part of the Airbase package

---
Wireless Fingerprinting
Wireless Fingerprinting
- Tool used to remotely find make and model of WNIC
- Traditionally auditors attempt to guess make and model of wireless device by using the device’s MAC address
  - Unreliable since MAC can be spoofed
- Tools:
  - Jc-duration-printer
- Note:
  - New technology, still not proven

---
Specialized Wireless Auditing LiveCD Toolkit
Specialized Wireless Auditing LiveCD Toolkit
- Compresses the entirety of the Linux operating system and environment into a single disc media
- Allows for a “live” instance of linux that can be loaded onto a Windows machine and run wireless auditing tools
- This can be used with versions of Linux that are specifically designed for frame-injection and wireless auditing

---
Defending Against Auditing &
Hacking Platform Assembly
Defending Against Auditing &
Hacking Platform Assembly
- It’s impossible to completely defend against hacking and auditing tools
- Anyone is free to create auditing and hacking tools
  - Nothing inherently wrong with those
- Creating laws to make it illegal to create auditing and hacking tools won’t do much and would hurt white hat hackers
  - Countries have tried (ie. Germany)

---
Wireless Infrastructure Auditing
Wireless Infrastructure Auditing
There are various technical activities for auditing wireless infrastructure:
- RF spectrum analysis
- Wireless infrastructure device identification
- Cracking encryption
- Layer 3 connectivity testing
- RF propagation boundaries
- DoS/hijacking

---
RF Spectrum Analysis
RF Spectrum Analysis
- You can use RF Spectrum Analysis to identify RF signals outside of your normal operating range
- Ex. If a company operates APs on Channels 1, 6, & 11 and during an audit notice RF signals that operate on Channel 13 & 14 an attacker might be running a rogue AP on the network that most WNIC would not see due to operating out of range
  - Also running on channel 13 & 14 violates FCC rules

---
Wireless Infrastructure Device Identification
Wireless Infrastructure Device Identification
Identify devices by analyzing layer 2 information
  - Ex. Use a tool like Kismet & Airodump-ng
- Kismet can
  - Detect wireless networks (802.11/a/b/g)
  - Sniff traffic
  - Offers limited intrusion detection capabilities
  - Works with an WNIC supporting raw RF monitoring (RFMON)

---
Wireless Infrastructure Device Identification (cont.)
Wireless Infrastructure Device Identification (cont.)
Using tools like Kismet you can find information like:
  - SSID (ESSID)
  - BSSID (MAC-48 convention ID)
  - RF Channel
  - Supported Rates
  - Wireless clients connected

---
Cracking Encryption
Cracking Encryption
- Multiple methods and tools exists to crack WEP/WPA/WPA2
- Airsnort & Dwepcrack
  - First generation WEP crackers work by capturing millions of packets to find patterns
- Aircrack-ng
  - Second generation WEP crackers that only require capturing a few hundred packets to find patterns
- Aireply-ng
  - Used to inject packets into connection to crack encryption

---
Cracking Encryption (cont.)
Cracking Encryption (cont.)
Airdecap-ng
  - Decrypts WEP/WPA capture files (.cap)
- Packetforge-ng
  - Used to forge wireless frames

---
Cracking Encryption (cont.)
Cracking Encryption (cont.)
WPA made cracking wireless encryption slightly harder but was more of a patch for really weak WEP
  - Improved WEP by using Temporal Key Integrity Protocol (TKIP)
  - Added 802.1x access control mechanism
  - Extensible Authentication Protocol (EAP)
- WPA2 was much stronger
  - Implemented 802.11i spec
  - Introduced AES-based algorithm
  - Counter-mode
  - CBC-MAC Protocol (CCMP)

---
Cracking Encryption (cont.)
Cracking Encryption (cont.)
- WPA-Enterprise offers more protection by using authentication server
- WPA-PSK offer more protection by using pre-shared key
Not in the book:
WPA2 was recently exploited (Oct. 2017) using KRACK , WPA3 in the works

---
Layer 3 Connectivity Testing
Layer 3 Connectivity Testing
- A number of tools and methods exists to get your device on a network and find other clients to attack
- Auditors can bypass MAC filtering on APs by using existing “allowed” wireless clients connected to AP
  - Tools: Airodump-ng and Probemapper scan for currently “allowed” clients connected to AP that you as an auditor can use
- Auditors can obtain a “legit” IP addresses by capturing data frames using tools like Wireshark and/or Tcpdump to determine a range of IP addresses the network uses
  - Note: Assuming network is unencrypted or cracked

---
Layer 3 Connectivity Testing (cont.)
Layer 3 Connectivity Testing (cont.)
Once on the network uses tools like Nmap to scan for open ports to potential services which can be compromised

---
RF Propagation Boundaries
RF Propagation Boundaries
- Audit used to determine the range RF signals reach from an AP
- Might seem simple and pointless, however, limiting the range an AP broadcast can help secure network
  - If attacker needs to be close enough to network then those operating the network might visually see threat
  - Can also be helpful when trying to create a timeline of a suspected wireless intrusion and determining time & place of attack

---
Denial of Service/Hijacking
Denial of Service/Hijacking
- Can occur on several layers of the wireless protocol
- RF jamming
  - Type of DoS by sending more powerful RF signal that drowns out other wireless signals
- Protocol DoS / Layer 2 DoS
  - Edit management and control frames sent to client, causing client to loss connection
    - Most clients don’t validate management and control frames and sending packets that seems to come from a legit AP with request to disconnect can trick the client into disconnecting from the AP (Use WLAN-Jack & Aireplay-ng to do this)

---
Denial of Service/Hijacking (cont.)
Denial of Service/Hijacking (cont.)
Flooding
  - Flood AP with fake clients, making it impossible for real clients to connect; Tools: File2air, Void11, MDK2, and MDK3
- Evil Twin (ph00ling)
  - Client connects to fake AP thinking it’s the real AP, Tools: Airsnarf
  - Or manually by
    - Setting WNIC in master mode
    - Configuring a HTTPD server to serve pages matching the captive portal of the spoofed service
    - Establishing a DHCPD and DNS server so the victim receives the IP address attack chooses for them

---
Practical Wireless Deployment Methodology (PWDM)
Practical Wireless Deployment Methodology (PWDM)
1. Deployment analysis
2. Contractual negotiation
3. Deployment tactical planning
4. Deployment procedural rollout
5. Supporting infrastructure rollout
6. AP security issues
7. Layer 3 mitigation strategies
8. Gateway management
9. Management overlay issues
10. UAT and commissioning
PWDN is designed to help any size organization deploying a WLAN to consistently and effectively by following a series of steps that cover many aspects of WLAN and WLAN security.
More at http://pwdm.net

---
Using Linux to Deliver Secure Wireless Infrastructure Devices
Using Linux to Deliver Secure Wireless Infrastructure Devices

---
Wireless Access Point
Wireless Access Point
You can DIY your own AP
  - Offers more customization and control
- 3 Solutions
  - Hostapd
    - Software only solution
  - OpenWRT/DD-WRT
    - Extends existing hardware like the Linksys WRT Router
  - Combined Stack
    - Mix software solutions like Soekris, PC Engine WRAP Board, Pyramid Linux and a variety of other Linux based router software to enable existing or new chipsets

---
Authentication Server
Authentication Server
Linux offers software solutions like FreeRADIUS to add backend authentication server to WPA/WPA2

---
Captive Portal
Captive Portal
- Captive Portals offer business, or anyone running an AP to regulate access with their AP either by requiring authentication or accepting terms and usage rules.
- Linux offers Free Software solutions like wifidog and NoCatAuth to implement on Linux based APs.

---
Wireless Intrusion Detection System (WIDS)
Wireless Intrusion Detection System (WIDS)
- Wireless IDS work like regular IDS but, well… for wireless
- WIDS requires more tools that can cover
  - Attacks using deauthentication packet floods
  - Detecting fake APs & captive portals
- Free Software solutions for IDS/WIDS are:
  - Snort
  - Snort-Wireless
    - Simply setup a Linux machine with a wireless card in RFMON mode and start using Snort
  - Kismet Wireless
  - WIDZ

---
Incident Response Kit
Incident Response Kit
Use Linux laptops with various tools during a incident response to find rogue AP
  - wavemon
    - Terminal (ncurses-based) wireless network monitor
  - probemapper
    - Map network based on strength of AP and physical barriers
- Other tools
  - OSWA-Assistant
    - Wireless auditing toolkit
  - Iperf
    - Wireless network performance monitoring tool

---
Wireless Client Auditing (Steps)
Wireless Client Auditing (Steps)
Wireless client fingerprinting
  - Determine the wireless chipset & driver
  - Use information to harden known vulnerabilities
- Wireless client profiling
  - Identify the various wireless clients that are sending data
  - Helps to find gaps in network policies for connecting clients
- Wireless client connect
  - Verify all connecting clients are following network policies set in place

---
Ending Notes
1. Everything can be hacked
2. Everything should be secured
3. Everything should be audited
Ending Notes